## Slide 1
VisionGuard
Real-Time Depth-Aware Object Detection
and Risk Analysis Prediction
Deep Learning Project
No LiDAR
Camera Only
Indian Roads
K.Tanya [160123748018]
1. YOLO Detection
2. Depth Estimation
3. TTC Calculator
4. Conditions Detect
5. RL Alert Agent
Complete AI Pipeline

## Slide 2
Problem Statement
1,53,972
Road accident deaths
India — 2021
LiDAR too expensive
Tesla ADAS uses LiDAR/Radar costing $4,000–$75,000 per unit — unaffordable for most Indians
Indian roads ignored
Existing models trained on western COCO dataset — no autorickshaws, cattle, or overloaded bikes
No adverse conditions
Most ADAS systems fail in night, rain, and fog — critical for Indian monsoon driving
VisionGuard solves all three — using only a camera.

## Slide 3
Our Solution — VisionGuard
Feature
Tesla ADAS
Mobileye
VisionGuard
Hardware
LiDAR + Radar + Cam
Proprietary chip
Single RGB Camera
Cost
$10,000+
$1,000+
~$0
Indian Classes
✗ No
✗ No
✓ Yes
Night / Rain
Partial
Partial
✓ Detected
RL Alert Policy
✗ Rule-based
✗ Rule-based
✓ PPO Trained
Camera-Only ADAS — Making Road Safety Accessible to Every Indian Vehicle Owner

## Slide 4
System Architecture
1
VIDEO INPUT
Camera / Phone / Video file
2
YOLO DETECTION
Fine-tuned on Indian roads
3
DEPTH ESTIMATION
DepthAnything v2 (no sensor)
4
TTC CALCULATOR
Regression on distance history
5
CONDITIONS DETECT
Night / Rain / Fog / Glare
6
RL ALERT AGENT
PPO policy — 200K steps
7
OVERLAY OUTPUT
Boxes + Alerts + Dashboard
All 7 modules run in a single loop — processing each frame from any video or live camera feed in real time

## Slide 5
Dataset & YOLO Fine-Tuning
3,438
Training Images
749
Validation Images
10
Indian Road Classes
50
Training Epochs
Per-Class Detection Accuracy (AP50)
bike
99.5%
autorickshaw
98.4%
car
96.7%
bus
95.0%
bicycle
88.8%
motorbike
80.0%
person
5.2%
Overall mAP50: 0.777

## Slide 6
Monocular Depth Estimation
DepthAnything v2 infers 3D scene structure from a single 2D camera frame — no LiDAR, no radar, no depth sensor needed
1
RGB frame captured from camera
2
DepthAnything v2 Small generates per-pixel depth map
3
For each YOLO bounding box, median depth of center region is extracted
4
Depth value converted to approximate distance in metres
5
Distance feeds into TTC calculator and risk scorer
Distance Accuracy
0 – 10 m
85–88%
10 – 20 m
79–85%
20 – 30 m
70–79%
30 – 40 m
60–70%
> 40 m
< 60%
Most accurate in 0–20m critical safety zone

## Slide 7
Reinforcement Learning Alert Agent
Why RL?
Rule-based alerts cause alert fatigue — drivers ignore them.
Our PPO agent learns WHEN and HOW urgently to alert,
balancing missed alerts (dangerous) vs false alarms (annoying).
Observation Space
[0] Distance (metres)
[1] TTC (seconds)
[2] Object class (0–9)
[3] Weather code (0–3)
[4] Time of day (0–1)
4 Alert Actions
0
NO ALERT
TTC > 10s, dist > 35m
Max reward: +5
1
CAUTION
TTC 6–10s, dist 20–35m
Max reward: +8
2
WARNING!
TTC 2.5–6s, dist 10–20m
Max reward: +15
3
BRAKE NOW!
TTC < 2.5s, dist < 8m
Max reward: +20
Trained: 200,000 timesteps | Algorithm: PPO | Framework: Stable-Baselines3

## Slide 8
Results & Performance
0.777
Overall mAP50
Object Detection
0.984
Autorickshaw AP50
Best Indian class
200K
RL Training Steps
PPO agent trained
4.2ms
Inference Speed
Per frame on GPU
RL Agent Decision Accuracy
Scenario
Agent Decision
Reward
Car very close (4m, TTC 1s)
BRAKE NOW!
+20
Pedestrian approaching (7m)
BRAKE NOW!
+20
Car at night (8m, TTC 3s)
BRAKE NOW!
+20
Car far away (35m, TTC 15s)
NO ALERT
+5
Everything safe (50m)
NO ALERT
+5

## Slide 12
Live Demo — VisionGuard UI
What the Demo Shows:
📁 Upload dashcam video or connect phone camera via IP Webcam app
📦 YOLO detects objects — cars, bikes, autorickshaws — in real time
📏 Distance shown in metres on every bounding box
⏱️ TTC (Time-to-Collision) updates live as objects approach
🔴 Risk score bar (0–100) updates every frame
🔔 RL agent triggers CAUTION / WARNING / BRAKE NOW alerts
🌙 Night / Rain / Fog automatically detected and displayed
Phone Camera Setup (IP Webcam):
1
Install IP Webcam app on Android phone
2
Open app → tap Start Server
3
Note IP address shown on screen
(e.g. http://192.168.1.5:8080)
4
Select Phone Camera in VisionGuard UI
5
Enter IP → click Connect & Start
6
Point phone at traffic — live detection!

## Slide 13
Conclusion & Future Work
What We Built:
✓ Fine-tuned YOLOv8 on 3,438 Indian road images — mAP50: 0.777
✓ Monocular depth estimation replacing LiDAR — distance in metres
✓ Time-to-Collision calculator using velocity regression
✓ Adverse conditions detector (night, rain, fog, glare)
✓ PPO RL agent — 200,000 step trained alert policy
✓ Streamlit web UI with phone camera live mode
Future Work:
→ Deploy on Raspberry Pi 5 for real vehicle
→ Add lane detection module
→ Improve person & tractor detection
→ Test in CARLA driving simulator
→ DeepSORT tracking for stable TTC
→ Speed estimation per vehicle
VisionGuard — Making ADAS Accessible to Every Indian Vehicle Owner
Camera Only | No LiDAR | No Radar | ~Min Cost | Built for Indian Roads